Report:

The provided code includes a section that implements floor division using machine code. Step-by-step explanation of the code for floor division:
1. In state 3'b110, the address addr_toRAM is set to the current program counter (PC), and the next state stN is set to 3'h111.
2. In state 3'b111, the instruction from the memory (data_fromRAM) is loaded into the immediate value IWN.
3. The code then checks the opcode and operands of the loaded instruction using if statements.
4. If the opcode is 0010 (CPi instruction) and the operand is 000000000001 (immediate value of 1), the address addr_toRAM is set to 0, and the next state stN is set to 3'h1000.
5. If the opcode is 0001 (ADDi instruction), the address addr_toRAM is set to 0, and the next state stN is set to 3'h1001.
6. If the opcode matches the opcodes of ADD, ADDi, NAND, NANDi, BZJi, or BZJ instructions (00 or 110), the operand opA is extracted from the instruction and stored in addr_toRAM. The next state stN is set to 3'b010.
7. In state 3'b1000, the division operation is performed by subtracting the operand (data_fromRAM) from the accumulator (A). The program counter (PC) is incremented, the address addr_toRAM is set to 0, and the next state stN is set to 3'h1010.
8. In state 3'b1001, the addition operation is performed by adding the operand (data_fromRAM) to the accumulator (A). The program counter (PC) is incremented, the address addr_toRAM is set to 0, and the next state stN is set to 3'h1010.
9. In state 3'b1010, the result of the division operation is stored in data_toRAM, and the write enable signal wrEn is set to 1 to write the result back to the memory. The program counter (PC) is incremented, and the next state stN is determined based on the interrupt and interrupt service routine (ISR) conditions.
10. If an interrupt is pending (intr == 1'b1) and the ISR is not active (isr != 1'b1), the next state stN is set to 3'h4 to handle the ISR.
11. Otherwise, the next state stN is set to 3'h0 to continue normal execution.

State 000: Reset state. Initializes all registers and signals.
State 001: Fetch instruction. Reads the instruction from RAM at the address specified by the program counter (PC).
State 010: Decode instruction. Determines the type of instruction and performs appropriate actions based on the instruction opcode.
State 011: Execute instruction. Performs the execution of instructions like ADD, ADDi, NAND, NANDi, and BZJ.
State 100: Get Interrupt Service Routine (ISR) address. Reads the ISR address from RAM.
State 101: Store the next instruction address. Writes the current program counter value to RAM. State 110: Fetch instruction for the floor division machine code.
State 111: Decode instruction for the floor division machine code.
States 1000, 1001, and 1010: Modified states for floor division machine code execution.

-----------------------------------------------------------------------------------------------------------
Timing Summary:
---------------
Speed Grade: -3

   Minimum period: 2.643ns (Maximum Frequency: 378.372MHz)
   Minimum input arrival time before clock: 2.989ns
   Maximum output required time after clock: 3.324ns
   Maximum combinational path delay: 2.907ns

Area Synthesis Results

Advanced HDL Synthesis Report

Macro Statistics
# Adders/Subtractors : 4
 14-bit adder : 2
 32-bit adder : 2
# Registers : 80
 Flip-Flops : 80
# Multiplexers : 28
 1-bit 2-to-1 multiplexer : 5
 14-bit 2-to-1 multiplexer : 14
 14-bit 8-to-1 multiplexer : 1
 32-bit 2-to-1 multiplexer : 6
 32-bit 4-to-1 multiplexer : 2
# FSMs : 1

 HDL Synthesis
    States 6
    | Transitions 23
    | Inputs 13
    | Outputs 5
    | Clock clk (rising_edge)
    | Reset rst (positive)
    | Reset type synchronous
    | Reset State 000
    | Encoding auto
    | Implementation LUT

Final Register Report

Macro Statistics
# Registers : 84
 Flip-Flops : 84

 Design Summary

Clock Information:
Clock Signal | Clock buffer(FF name) | Load
clk | BUFGP | 84

********************************************************************************

Copyright (c) 1995-2013 Xilinx, Inc. All rights reserved.
--> Parameter TMPDIR set to xst/projnav.tmp

Total REAL time to Xst completion: 0.00 secs
Total CPU time to Xst completion: 0.09 secs

--> Parameter xsthdpdir set to xst

Total REAL time to Xst completion: 0.00 secs
Total CPU time to Xst completion: 0.09 secs

--> Reading design: VerySimpleCPU.prj

TABLE OF CONTENTS
  1) Synthesis Options Summary
  2) HDL Parsing
  3) HDL Elaboration
  4) HDL Synthesis
       4.1) HDL Synthesis Report
  5) Advanced HDL Synthesis
       5.1) Advanced HDL Synthesis Report
  6) Low Level Synthesis
  7) Partition Report
  8) Design Summary
       8.1) Primitive and Black Box Usage
       8.2) Device utilization summary
       8.3) Partition Resource Summary
       8.4) Timing Report
        8.4.1) Clock Information
        8.4.2) Asynchronous Control Signals Information
        8.4.3) Timing Summary
        8.4.4) Timing Details
        8.4.5) Cross Clock Domains Report

=========================================================================
* Synthesis Options Summary *
=========================================================================
---- Source Parameters
Input File Name : "VerySimpleCPU.prj"
Ignore Synthesis Constraint File : NO

---- Target Parameters
Output File Name : "VerySimpleCPU"
Output Format : NGC
Target Device : xc7a100t-3-csg324

---- Source Options
Top Module Name : VerySimpleCPU
Automatic FSM Extraction : YES
FSM Encoding Algorithm : Auto
Safe Implementation : No
FSM Style : LUT
RAM Extraction : Yes
RAM Style : Auto
ROM Extraction : Yes
Shift Register Extraction : YES
ROM Style : Auto
Resource Sharing : YES
Asynchronous To Synchronous : NO
Shift Register Minimum Size : 2
Use DSP Block : Auto
Automatic Register Balancing : No

---- Target Options
LUT Combining : Auto
Reduce Control Sets : Auto
Add IO Buffers : YES
Global Maximum Fanout : 100000
Add Generic Clock Buffer(BUFG) : 32
Register Duplication : YES
Optimize Instantiated Primitives : NO
Use Clock Enable : Auto
Use Synchronous Set : Auto
Use Synchronous Reset : Auto
Pack IO Registers into IOBs : Auto
Equivalent register Removal : YES

---- General Options
Optimization Goal : Speed
Optimization Effort : 1
Power Reduction : NO
Keep Hierarchy : No
Netlist Hierarchy : As_Optimized
RTL Output : Yes
Global Optimization : AllClockNets
Read Cores : YES
Write Timing Constraints : NO
Cross Clock Analysis : NO
Hierarchy Separator : /
Bus Delimiter : <>
Case Specifier : Maintain
Slice Utilization Ratio : 100
BRAM Utilization Ratio : 100
DSP48 Utilization Ratio : 100
Auto BRAM Packing : NO
Slice Utilization Ratio Delta : 5

=========================================================================

=========================================================================
* HDL Parsing *
=========================================================================
Analyzing Verilog file "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" into library work
Parsing module <VerySimpleCPU>.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 160: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 166: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 170: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 178: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 182: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 184: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 188: Constant value is truncated to fit in <3> bits.
WARNING:HDLCompiler:568 - "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v" Line 190: Constant value is truncated to fit in <3> bits.

=========================================================================
* HDL Elaboration *
=========================================================================

Elaborating module <VerySimpleCPU>.

=========================================================================
* HDL Synthesis *
=========================================================================

Synthesizing Unit <VerySimpleCPU>.
    Related source file is "C:\.Xilinx\VerySimpleCPU_HW\VerySimpleCPU.v".
    Found 14-bit register for signal <PC>.
    Found 32-bit register for signal <A>.
    Found 32-bit register for signal <IW>.
    Found 1-bit register for signal <intr>.
    Found 1-bit register for signal <isr>.
    Found 3-bit register for signal <st>.
    Found finite state machine <FSM_0> for signal <st>.
    -----------------------------------------------------------------------
    | States | 6 |
    | Transitions | 23 |
    | Inputs | 13 |
    | Outputs | 5 |
    | Clock | clk (rising_edge) |
    | Reset | rst (positive) |
    | Reset type | synchronous |
    | Reset State | 000 |
    | Encoding | auto |
    | Implementation | LUT |
    -----------------------------------------------------------------------
    Found 32-bit adder for signal <data_fromRAM[31]_GND_1_o_add_21_OUT> created at line 81.
    Found 14-bit adder for signal <data_fromRAM[13]_IW[13]_add_42_OUT> created at line 101.
    Found 32-bit adder for signal <A[31]_data_fromRAM[31]_add_49_OUT> created at line 111.
    Found 14-bit adder for signal <PC[13]_GND_1_o_add_50_OUT> created at line 113.
    Found 14-bit 8-to-1 multiplexer for signal <addr_toRAM> created at line 62.
    Found 32-bit 4-to-1 multiplexer for signal <_n0171> created at line 90.
    Found 32-bit 4-to-1 multiplexer for signal <_n0180> created at line 119.
    Summary:
inferred 4 Adder/Subtractor(s).
inferred 80 D-type flip-flop(s).
inferred 28 Multiplexer(s).
inferred 1 Finite State Machine(s).
Unit <VerySimpleCPU> synthesized.

=========================================================================
HDL Synthesis Report

Macro Statistics
# Adders/Subtractors : 4
 14-bit adder : 2
 32-bit adder : 2
# Registers : 5
 1-bit register : 2
 14-bit register : 1
 32-bit register : 2
# Multiplexers : 28
 1-bit 2-to-1 multiplexer : 5
 14-bit 2-to-1 multiplexer : 14
 14-bit 8-to-1 multiplexer : 1
 32-bit 2-to-1 multiplexer : 6
 32-bit 4-to-1 multiplexer : 2
# FSMs : 1

=========================================================================

=========================================================================
* Advanced HDL Synthesis *
=========================================================================

=========================================================================
Advanced HDL Synthesis Report

Macro Statistics
# Adders/Subtractors : 4
 14-bit adder : 2
 32-bit adder : 2
# Registers : 80
 Flip-Flops : 80
# Multiplexers : 28
 1-bit 2-to-1 multiplexer : 5
 14-bit 2-to-1 multiplexer : 14
 14-bit 8-to-1 multiplexer : 1
 32-bit 2-to-1 multiplexer : 6
 32-bit 4-to-1 multiplexer : 2
# FSMs : 1

=========================================================================

=========================================================================
* Low Level Synthesis *
=========================================================================
Analyzing FSM <MFsm> for best encoding.
Optimizing FSM <FSM_0> on signal <st[1:3]> with user encoding.
-------------------
 State | Encoding
-------------------
 000 | 000
 001 | 001
 010 | 010
 011 | 011
 100 | 100
 101 | 101
-------------------

Optimizing unit <VerySimpleCPU> ...

Mapping all equations...
Building and optimizing final netlist ...
Found area constraint ratio of 100 (+ 5) on block VerySimpleCPU, actual ratio is 0.
FlipFlop st_FSM_FFd3 has been replicated 1 time(s)

Final Macro Processing ...

=========================================================================
Final Register Report

Macro Statistics
# Registers : 84
 Flip-Flops : 84

=========================================================================

=========================================================================
* Partition Report *
=========================================================================

Partition Implementation Status
-------------------------------

  No Partitions were found in this design.

-------------------------------

=========================================================================
* Design Summary *
=========================================================================

Top Level Output File Name : VerySimpleCPU.ngc

Primitive and Black Box Usage:
------------------------------
# BELS : 503
# GND : 1
# INV : 1
# LUT1 : 31
# LUT2 : 63
# LUT3 : 8
# LUT4 : 32
# LUT5 : 52
# LUT6 : 132
# MUXCY : 88
# MUXF7 : 2
# VCC : 1
# XORCY : 92
# FlipFlops/Latches : 84
# FDR : 36
# FDRE : 48
# Clock Buffers : 1
# BUFGP : 1
# IO Buffers : 81
# IBUF : 34
# OBUF : 47

Device utilization summary:
---------------------------

Selected Device : 7a100tcsg324-3

Slice Logic Utilization:
 Number of Slice Registers: 84 out of 126800 0%
 Number of Slice LUTs: 319 out of 63400 0%
    Number used as Logic: 319 out of 63400 0%

Slice Logic Distribution:
 Number of LUT Flip Flop pairs used: 335
   Number with an unused Flip Flop: 251 out of 335 74%
   Number with an unused LUT: 16 out of 335 4%
   Number of fully used LUT-FF pairs: 68 out of 335 20%
   Number of unique control sets: 7

IO Utilization:
 Number of IOs: 82
 Number of bonded IOBs: 82 out of 210 39%

Specific Feature Utilization:
 Number of BUFG/BUFGCTRLs: 1 out of 32 3%

---------------------------
Partition Resource Summary:
---------------------------

  No Partitions were found in this design.

---------------------------

=========================================================================
Timing Report

NOTE: THESE TIMING NUMBERS ARE ONLY A SYNTHESIS ESTIMATE.
      FOR ACCURATE TIMING INFORMATION PLEASE REFER TO THE TRACE REPORT
      GENERATED AFTER PLACE-and-ROUTE.

Clock Information:
------------------
-----------------------------------+------------------------+-------+
Clock Signal | Clock buffer(FF name) | Load |
-----------------------------------+------------------------+-------+
clk | BUFGP | 84 |
-----------------------------------+------------------------+-------+

Asynchronous Control Signals Information:
----------------------------------------
No asynchronous control signals found in this design

Timing Summary:
---------------
Speed Grade: -3

   Minimum period: 2.643ns (Maximum Frequency: 378.372MHz)
   Minimum input arrival time before clock: 2.989ns
   Maximum output required time after clock: 3.324ns
   Maximum combinational path delay: 2.907ns

Timing Details:
---------------
All values displayed in nanoseconds (ns)

=========================================================================
Timing constraint: Default period analysis for Clock 'clk'
  Clock period: 2.643ns (frequency: 378.372MHz)
  Total number of paths / destination ports: 979 / 134
-------------------------------------------------------------------------
Delay: 2.643ns (Levels of Logic = 17)
  Source: IW_0 (FF)
  Destination: PC_13 (FF)
  Source Clock: clk rising
  Destination Clock: clk rising

  Data Path: IW_0 to PC_13
        Gate Net
    Cell:in->out fanout Delay Delay Logical Name (Net Name)
    ---------------------------------------- ------------
     FDRE:C->Q 4 0.361 0.309 IW_0 (IW_0)
     LUT2:I1->O 1 0.097 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_lut<0> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_lut<0>)
     MUXCY:S->O 1 0.353 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<0> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<0>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<1> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<1>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<2> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<2>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<3> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<3>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<4> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<4>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<5> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<5>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<6> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<6>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<7> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<7>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<8> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<8>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<9> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<9>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<10> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<10>)
     MUXCY:CI->O 1 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<11> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<11>)
     MUXCY:CI->O 0 0.023 0.000 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<12> (Madd_data_fromRAM[13]_IW[13]_add_42_OUT_cy<12>)
     XORCY:CI->O 1 0.370 0.295 Madd_data_fromRAM[13]_IW[13]_add_42_OUT_xor<13> (data_fromRAM[13]_IW[13]_add_42_OUT<13>)
     LUT6:I5->O 1 0.097 0.379 Mmux_PCN102 (Mmux_PCN101)
     LUT4:I2->O 1 0.097 0.000 Mmux_PCN103 (PCN<13>)
     FDRE:D 0.008 PC_13
    ----------------------------------------
    Total 2.643ns (1.659ns logic, 0.984ns route)
        (62.8% logic, 37.2% route)

=========================================================================
Timing constraint: Default OFFSET IN BEFORE for Clock 'clk'
  Total number of paths / destination ports: 1255 / 163
-------------------------------------------------------------------------
Offset: 2.989ns (Levels of Logic = 5)
  Source: data_fromRAM<13> (PAD)
  Destination: PC_0 (FF)
  Destination Clock: clk rising

  Data Path: data_fromRAM<13> to PC_0
        Gate Net
    Cell:in->out fanout Delay Delay Logical Name (Net Name)
    ---------------------------------------- ------------
     IBUF:I->O 9 0.001 0.730 data_fromRAM_13_IBUF (data_fromRAM_13_IBUF)
     LUT6:I0->O 1 0.097 0.693 data_fromRAM[31]_GND_1_o_equal_71_o<31>1 (data_fromRAM[31]_GND_1_o_equal_71_o<31>)
     LUT6:I0->O 28 0.097 0.789 data_fromRAM[31]_GND_1_o_equal_71_o<31>7 (data_fromRAM[31]_GND_1_o_equal_71_o)
     LUT5:I0->O 1 0.097 0.379 Mmux_PCN181 (Mmux_PCN18)
     LUT4:I2->O 1 0.097 0.000 Mmux_PCN183 (PCN<4>)
     FDRE:D 0.008 PC_4
    ----------------------------------------
    Total 2.989ns (0.397ns logic, 2.592ns route)
        (13.3% logic, 86.7% route)

=========================================================================
Timing constraint: Default OFFSET OUT AFTER for Clock 'clk'
  Total number of paths / destination ports: 2150 / 47
-------------------------------------------------------------------------
Offset: 3.324ns (Levels of Logic = 36)
  Source: A_0 (FF)
  Destination: data_toRAM<31> (PAD)
  Source Clock: clk rising

  Data Path: A_0 to data_toRAM<31>
        Gate Net
    Cell:in->out fanout Delay Delay Logical Name (Net Name)
    ---------------------------------------- ------------
     FDR:C->Q 3 0.361 0.389 A_0 (A_0)
     LUT2:I0->O 1 0.097 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_lut<0> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_lut<0>)
     MUXCY:S->O 1 0.353 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<0> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<0>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<1> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<1>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<2> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<2>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<3> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<3>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<4> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<4>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<5> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<5>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<6> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<6>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<7> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<7>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<8> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<8>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<9> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<9>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<10> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<10>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<11> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<11>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<12> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<12>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<13> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<13>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<14> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<14>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<15> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<15>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<16> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<16>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<17> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<17>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<18> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<18>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<19> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<19>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<20> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<20>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<21> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<21>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<22> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<22>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<23> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<23>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<24> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<24>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<25> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<25>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<26> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<26>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<27> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<27>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<28> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<28>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<29> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<29>)
     MUXCY:CI->O 0 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<30> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<30>)
     XORCY:CI->O 1 0.370 0.295 Madd_A[31]_data_fromRAM[31]_add_49_OUT_xor<31> (A[31]_data_fromRAM[31]_add_49_OUT<31>)
     LUT6:I5->O 1 0.097 0.295 Mmux_data_toRAM251 (Mmux_data_toRAM25)
     LUT6:I5->O 1 0.097 0.279 Mmux_data_toRAM252 (data_toRAM_31_OBUF)
     OBUF:I->O 0.000 data_toRAM_31_OBUF (data_toRAM<31>)
    ----------------------------------------
    Total 3.324ns (2.065ns logic, 1.259ns route)
        (62.1% logic, 37.9% route)

=========================================================================
Timing constraint: Default path analysis
  Total number of paths / destination ports: 1501 / 46
-------------------------------------------------------------------------
Delay: 2.907ns (Levels of Logic = 37)
  Source: data_fromRAM<0> (PAD)
  Destination: data_toRAM<31> (PAD)

  Data Path: data_fromRAM<0> to data_toRAM<31>
        Gate Net
    Cell:in->out fanout Delay Delay Logical Name (Net Name)
    ---------------------------------------- ------------
     IBUF:I->O 9 0.001 0.332 data_fromRAM_0_IBUF (data_fromRAM_0_IBUF)
     LUT2:I1->O 1 0.097 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_lut<0> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_lut<0>)
     MUXCY:S->O 1 0.353 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<0> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<0>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<1> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<1>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<2> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<2>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<3> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<3>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<4> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<4>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<5> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<5>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<6> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<6>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<7> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<7>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<8> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<8>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<9> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<9>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<10> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<10>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<11> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<11>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<12> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<12>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<13> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<13>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<14> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<14>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<15> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<15>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<16> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<16>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<17> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<17>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<18> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<18>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<19> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<19>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<20> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<20>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<21> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<21>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<22> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<22>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<23> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<23>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<24> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<24>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<25> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<25>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<26> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<26>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<27> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<27>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<28> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<28>)
     MUXCY:CI->O 1 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<29> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<29>)
     MUXCY:CI->O 0 0.023 0.000 Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<30> (Madd_A[31]_data_fromRAM[31]_add_49_OUT_cy<30>)
     XORCY:CI->O 1 0.370 0.295 Madd_A[31]_data_fromRAM[31]_add_49_OUT_xor<31> (A[31]_data_fromRAM[31]_add_49_OUT<31>)
     LUT6:I5->O 1 0.097 0.295 Mmux_data_toRAM251 (Mmux_data_toRAM25)
     LUT6:I5->O 1 0.097 0.279 Mmux_data_toRAM252 (data_toRAM_31_OBUF)
     OBUF:I->O 0.000 data_toRAM_31_OBUF (data_toRAM<31>)
    ----------------------------------------
    Total 2.907ns (1.705ns logic, 1.202ns route)
        (58.6% logic, 41.4% route)

=========================================================================

Cross Clock Domains Report:
--------------------------

Clock to Setup on destination clock clk
---------------+---------+---------+---------+---------+
        | Src:Rise| Src:Fall| Src:Rise| Src:Fall|
Source Clock |Dest:Rise|Dest:Rise|Dest:Fall|Dest:Fall|
---------------+---------+---------+---------+---------+
clk | 2.643| | | |
---------------+---------+---------+---------+---------+

=========================================================================

Total REAL time to Xst completion: 7.00 secs
Total CPU time to Xst completion: 7.57 secs

-->

Total memory usage is 4617888 kilobytes

Number of errors : 0 ( 0 filtered)
Number of warnings : 8 ( 0 filtered)
Number of infos : 0 ( 0 filtered)